MAMMOTH MTN. MET STATION

# Sensor Change/Maintenance Information

NOTE: Please document changes relating to sensors, including, but not limited to, installation, movement from one location or height to another, calibration, or retirement.  When finished, save file as YYYY-MM-DD (eg., 1999-09-17)

## Sensor Identification Information

| Type of Sensor: | Gamma ray device | Description: | Measure SWE |
| --- | --- | --- | --- |
| Manufacturer: | Canberra | Owner: | USACE/CRREL |
| Model: | NA | Property ID: | NA |
| Serial ID: | NA | Purchase Date: | October, 1999 |
| Nickname: |  | Grant: |  |
| Comments: | Ground level unit |

## Sensor Change/Maintenance Information

| Date: | 1999-10-26 |
| --- | --- |
| Person/Organization: | Tom Painter/Rick Kattelmann – ICESS/UCSB |
| Description*: | Unit emplacement in ground – 334 cm directly south of W edge bunker |

* If sensor calibrated, include slope, offset and drift.  If sensor moved, include position (eg. north of bunker) and height.

Additional Notes:

There is a pair of these units – one emplaced in the ground and buried, the other mounted on the platform.  This unit is buried 334 cm directly south of the second protrusion from the west on the south side of the bunker, almost directly below the depth sensor on the boom from the platform.  Plastic beaker supports the unit along with many rocks – minor dirt fill in the rocks, plastic sheet a few inches below surface and then dirt fill atop that.  Dirt fill tamped to reduce erosion.  This unit will measure gamma radiation – attenuation of signal due to snow water equivalent above.  To be compared with that baseline unit mounted on the platform.

As of 1999-10-25, the program to invert device signal for SWE is yet to be delivered.  Apparently, they (not sure who they are) are still quantifying the relationship.