MAMMOTH MTN. MET STATION

# Sensor Change/Maintenance Information

NOTE: Please document changes relating to sensors, including, but not limited to, installation, movement from one location or height to another, calibration, or retirement.  When finished, save file as YYYY-MM-DD (eg., 1999-09-17)

## Sensor Identification Information

| Type of Sensor: | Gamma ray device | Description: | Measure SWE |
| --- | --- | --- | --- |
| Manufacturer: | Canberra | Owner: | USACE/CRREL |
| Model: | NA | Property ID: |  |
| Serial ID: | 99090032 | Purchase Date: | October, 1999 |
| Nickname: |  | Grant: |  |
| Comments: | Platform level unit |

## Sensor Change/Maintenance Information

| Date: | 1999-10-26 |
| --- | --- |
| Person/Organization: | Tom Painter/Rick Kattelmann – ICESS/UCSB |
| Description*: | Unit mounted to platform rail, north side, 6 inches east of tube to bunker |

* If sensor calibrated, include slope, offset and drift.  If sensor moved, include position (eg. north of bunker) and height.

Additional Notes:

There is a pair of these units – this unit is mounted on the platform rail and will measure incoming gamma radiation as a baseline, the other unit is buried to just at ground level and will measure gamma radiation attenuated by the snowpack.  The unit is attached to the north rail of the platform, 17 cm east of the tube into the bunker.

As of 1999-10-25, the program to invert device signal for SWE is yet to be delivered.  Apparently, they (not sure who they are) are still quantifying the relationship.