MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | Jan 17, 2001 |
| --- | --- |
| Time: | 1100 |
| Name: | Sue Burak |

# CONDITIONS:

| Sky: | Clear, very cold |
| --- | --- |
| Wind: | NW |
| Temp: | -15 C |
| Snow Depth: | 130 |
| Rime? (Y or N): | N |

NOTES:  check on radiometers for Cool- ee.  All up radiometers working.

Measured and reset snowboards

Digital board: 35, 2.9.  wind layer 10 cm down.  Drifted snow on board, took average of depths and swe’s.

East board: 28, 2.6 wind layer 10 cm down

North board: 20, 1.5