MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 2001-02-22 |
| --- | --- |
| Time: | 1113h |
| Name: | Tom Painter |

# CONDITIONS:

| Sky: | Cloudy, snowing |
| --- | --- |
| Wind: | Gusty, 4 m/s |
| Temp: | -8 C |
| Snow Depth: | 220 platform, 267 I-beam |
| Rime? (Y or N): | N, but some icing |

NOTES:

Storm a’ comin- in – windy, snowing lightly.

Cleared digital board and storm boards.  Raised wind mast 2 pin holes.  Freed digital board and other cables from drifting.

SWE from boards:

Board		Depth (cm)	Density	SWE (cm)

Digital		57 		188.8		10.8

East		41 		182.0		7.5

North		51.5		202.0		10.4

Filed shaft on tube lid closure to make easier to open – it was getting such that any ice build up makes it almost impossible to open.  Whannnhhh!