MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 8/24/2001 |
| --- | --- |
| Time: | 1030 DST |
| Name: | Bryan Harrington |

# CONDITIONS:

| Sky: | Clear |
| --- | --- |
| Wind: | Light |
| Temp: | 17.7 C |
| Snow Depth: | 0 |
| Rime? (Y or N): | N |

NOTES:

## Power Supply for the snow pillow (JJ), settings 20 volt range

The power supply was being over-loaded V =  2 & I = .58 ,  removed red wire from 20 volt terminal and the voltage supply returned to V = 12 & I = 0. I’ll look into why?

Shipment was at Snarl.

Talked to Mr. Dawson about blowtorch to cut steel platform for rain gauge mounting.

I found the HP 6236B Power Supply covered with a storage module, COM200 modem and the PS512M power supply. I’ve removed the storage module and COM200 modem from the top of the HP 6236B Power Supply this supply needs airflow to cool.

Unpacked shipment

Rain gauge roughed up a little bit during shipping had to straighten it out and replace a part that had become dislodged from its mounting.

Removed the power at the platform AC outlet that was supplying 120 VAC to the rain gauge heater transformer. Removed the RM Young rain gauge. Sending it back to CRREL.

Set MD-9 that is connected to SWE data logger (21X), has an ID of 3. Installed MD-9 onto network.