MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished, save document as YYYY-MM-DD (eg, 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 8/28/01 |
| --- | --- |
| Time: | 1600 DST |
| Name: | Bryan Harrington |

# CONDITIONS:

| Sky: | 10% cloud, light cum |
| --- | --- |
| Wind: | Brisk |
| Temp: | 20.4 C |
| Snow Depth: | 0 |
| Rime? (Y or N): | N |

NOTES:

Calibrated the Belfort rain gauge with the data logger system (volts)

Calibration data in an Excel file stored under (E:) mmsa/Mammoth01/Calibration

Reworked the program for the CR7_2 and updated the MMSA Log Book system program area.

Powered up the Snowmons and data logger using the new power supply, the measurement snowmon powered up OK but the reference snowmon is not running right. NOT GOOD! Tried to call 2B Technologies, Inc. telephone number (303)-216-0489 no answer. The DCP voltage is supposed to ramp to 5 volts and then reset. The reference unit is not ramping. Will call again. May have been hurt during shipping as this is the one I worked with at CRREL.