MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 08/30/2001 |
| --- | --- |
| Time: | 1325 DST |
| Name: | Bryan Harrington |

# CONDITIONS:

| Sky: | Light cum |
| --- | --- |
| Wind: | Light, heavy in the late afternoon. |
| Temp: | 17.8 |
| Snow Depth: | 0 |
| Rime? (Y or N): | N |

NOTES:

The snow pillow (JJ) was removed today and I found that there is a short of 4.8 ohms in the red and black wire being used to connect the snow pillow to the power supply. The snow depth reading should have gone below zero, as the target surface is further away. The splice on the platform for the snow pillow cable was ok. Its resistance measured open. Short is some where in between the platform and the power supply. I’ve looked the cable over in the annex (bunker, war talk) and found it to look fine. It’s not the same cable I went up to the splice and put 1K-ohm resistor between red and white. Bingo the cable that’s been used inside of the annex is not the snow pillow cable. I’ve found the right one and labeled it SNOW PILLOW JJ and wired it into the power supply and data logger. Now, with the snow pillow attached to the data logger cable and some weight on the pillow the reading looks ok at least it is moving.

Put the six pin connector in the snow pillow cable.