MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 2002-09-11 |
| --- | --- |
| Time: | 1101 DST |
| Name: | Bryan Harrington/Jesse Stanley |

# CONDITIONS:

| Sky: | clear |
| --- | --- |
| Wind: | 1.6 m/s |
| Temp: | 60 F |
| Snow Depth: | none |
| Rime? (Y or N): | N |

NOTES: Installed temperature/relative humidity probe on platform.

Changed Mamwinds.csi program to reflect battery voltage measurement at program location 1 data stored in location 20.

Found Agilent power supply off, this supply powers the gamma radiation tube instrumentation and the 4 ea. soil moisture probes. Turned power supply on, set for 14 volts dc current drain at this time is .427 amps.

Found all snow depth sensors working, but needed to have offsets reset.

I changed offsets to snow depth sensors as follows.

sp_sndpth changed to 146

bm_sndpth changed to 511

wm_sndpth changed to 307

ib_sndpth changed to 474