MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 2002-9-16 |
| --- | --- |
| Time: | 1450 DST |
| Name: | Bryan Harrington/ Jesse Stanley/ John Fiori |

# CONDITIONS:

| Sky: | Clear |
| --- | --- |
| Wind: | 7.2 m/s |
| Temp: | 10.8 C |
| Snow Depth: | NA |
| Rime? (Y or N): | N |

NOTES: Installed the new computer, setup the Axis camera system, setup the FTP client server, setup the new UPS under the bench for the computer, printer, monitor, network Hub TP4Combo and Agilent power supply.

Rewired the backup 12 volts dc power supply to the CR7_1 & CR7_2, mounted a battery charger on the wall under the bench with the batteries. The charger will keep the backup battery charged then during an outage the battery will keep the data logging systems up and going until power is restored. We attempted to rewired two snow depth sensors for backup and

I’ve removed the snow pillow #2 from its mounting device for shipment back to CRREL along with two snow depth sensor.