MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 2000-04-27 |
| --- | --- |
| Time: | 1450 |
| Name: | Bert Davis |

# CONDITIONS:

| Sky: | Clear |
| --- | --- |
| Wind: | 5-10 ms-1 breezes |
| Temp: | 12 C |
| Snow Depth: | 2.9m at I beam |
| Rime? (Y or N): | N |

NOTES:

- Completed installing new mount for snow depth sensor on platform boom.  Vertical position of sensor now 2.5 cm lower than before.  Boom and snow depth sensor replaced in track to original position in the 1030-1100 timeframe.

- Performed first aid to snow disc (digital snow board).  Depth sensor back to original position and I’ve added a couple of different flavors of handle to the side.

- Dug snow pit near where we store the bamboo poles to calibrate the measurements of the Federal Sampler.  Total SWE in this pit will not prove representative of the site in general.