MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 2002-09-17 |
| --- | --- |
| Time: | 1420 DST |
| Name: | Bryan Harrington/ Jesse Stanley/ John Fiori |

# CONDITIONS:

| Sky: | Overcast |
| --- | --- |
| Wind: | 8 m/s |
| Temp: | 11 C |
| Snow Depth: | NA |
| Rime? (Y or N): | N |

NOTES: Mounted the second battery charger/ conditioner to the wall under the bench. The Agilent power supply was removed, because during an AC power failure the Agilent supply would not reboot. This supply is replaced by a deep cycle battery that is being conditioned by an AC power charger/ conditioner.

Jesse checked one of the small and the large tipping buckets for volume /tip. We found that the tipping buckets are not level and therefore the volume is different with each tip. It would be advisable to level the tipping buckets if you want quality data.

We repaired two collection bins for snow melt runoff, the sides were broken.

John reset the amount of time that the UPS would run before shutting down the computer. In a test it was found that the computer will not reboot upon the return of power. This is something that needs to be worked on.

We verified all the programs, in the logger, on hard copy and in the computer. We also checked the power point files and wiring diagrams for accuracy and updated as necessary.

I created a power point file to reflect the computer, UPS, printer, monitor and network Hub.

Jesse took pictures inside the annex.