MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | 10-14-2004 |
| --- | --- |
| Time: | 1300 |
| Name: | Jesse / Uphill |

# CONDITIONS:

| Sky: | clear |
| --- | --- |
| Wind: | no |
| Temp: | 14C |
| Snow Depth: | None |
| Rime? (Y or N): | NA |

NOTES:

Hard to believe the weather got BETTER.

Changed all PSP’s and PIR’s. Was one PIR short, so recycled uptherm2 to uptherm 1 because of most recent calibration. Re-installed battery when changed. Created spreadsheet document  PIR_PSP_Sensitivities_installed_04.xls under My Documents folder showing constants and serial numbers of units removed and units installed. Modified Campbell program to reflect constant changes and verified data.

Figured out how to change RH module electronics and sensor so Sue would be aware of how to make this change when new module is purchased, and old can be sent in for calibration. Took a couple of pictures demonstrating proper alignment of RH sensor in vane housing.

Verified Judd Depth sensors and adjusted offsets for near zero indication with no snow.