MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | Nov. 14, 2004 |
| --- | --- |
| Time: | 1000 |
| Name: | Sue Burak |

# CONDITIONS:

| Sky: | clear |
| --- | --- |
| Wind: | 4 m/s |
| Temp: | -3C |
| Snow Depth: | 113cm |
| Rime? (Y or N): | N |

NOTES:  Clear and cool. Tried another combination of silver tab/plastic tab on the wind dir. Still 180 degrees off.  Jammed it on, then pulled it off. Not sure what happened when Jesse changed bearings in October. Propeller nut came off. Store prop in metal trunk until I get proper replacement.

Adjsut shadowband, dig out around west side of bunker to uncover snow board poles. Tipping buckets tipping, both arrays. Pans still not draining unless encouraged by manually induced steeper gradient.