MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | Jan. 5, 2005 |
| --- | --- |
| Time: | 1000 |
| Name: | Sue Burak |

# CONDITIONS:

| Sky: | Partly cloudy |
| --- | --- |
| Wind: | 3 m/s |
| Temp: | -6C |
| Snow Depth: | 289cm |
| Rime? (Y or N): | N |

NOTES: First visit to site since Jan.1 and the 1 meter dump. Precip gauge over flowing. Total SWE 10 inches precip gauge. Changed glycol.

North Board: 75 cm, 11.5 cm SWE

Boom board:110 cm, 30.2 cm SWE

SE board: 102cm, 29.8 cm swe

Digging party.

Raised wind mast 1.5 meters. Wind mast snow depth sensor at snow surface. Changed offset at logger. Adjusted shadowband.