MAMMOTH MTN. MET STATION

Daily Journal

*NOTE:   When finished,  save document as YYYY-MM-DD (eg,. 1999-09-17), then print document and put it in “Daily Journal” section of MMSA Met Site notebook.

| Date: | June 29, 2006 |
| --- | --- |
| Time: | 7am – 4pm |
| Name: | MTC, Jesse |

# CONDITIONS:

| Sky: | Mostly clear |
| --- | --- |
| Wind: | Light |
| Temp: | +18C |
| Snow Depth: | Variable, 0-100cm? |
| Rime? (Y or N): | n |

NOTES:  Jesse and I rebuilt the platform I-Beam and it’s sensors, took off the plexi-glass and mounted all sensors directly to the bottom of the I-Beam.  This removed some weight and the “wing” effect of the plexiglass.  We think the support cables could be lighter and should have dual mount points on each side of the boom to minimize twisting. The surface temp sensor is hozed (Exergen) & needs replacing.  Replaced the platform depth sensor and reset to 411cm offset.  Measured around 53cm directly under it but surface is sloped toward bunker (north).

Took down the buggered I-Beam boom and will rebuild.  Probably 50cm of snow still under it.

Jesse noted some disconnected wires (ground wire on Exergen surface temp sensor) on CR7X2.