## Slide 1: Accuracy Requirements for Imaging Spectroscopy to Meet the Decadal Survey’s Most Important Objectives for Snow in the Water Cycle
Jeff Dozier, UC Santa Barbara David R. Thompson, JPL Edward H. (Ned) Bair, Leidos Niklas Bohn, JPL

## Slide 2: Background
Reflectivity (broadly defined) of deep snow
  Darker when grains are larger, mainly in the near-infrared
  Darker when contaminated by light-absorbing particles (LAP), mainly in the visible
  Usually different than other surfaces like vegetation or soil

## Slide 3
Illumination 60° Snow radii 50 to 1500 µm
Snow radius 1000 µm LAP conc. 10 to 500 ppmw
clean
Pine spectrum
Entisol spectrum
(from ECOSTRESS)

## Slide 4: What does the Decadal Survey say?
Specific need for measurement of snow albedo:
  “Spectral albedo of subpixel snow and glaciers at weekly intervals to an accuracy to estimate absorption of solar radiation to 10%”
Note that measurement of absorption to ±10% is a more stringent requirement than measuring albedo to that accuracy
  Consider an albedo of 0.8, so absorption (1–albedo) = 0.2. Reduce albedo by 10% (to 0.72), absorption = 0.28, an increase of 40%.
Implication: You really don’t care about albedo, you care about absorption (1–albedo)

## Slide 5
Illumination 60° Snow radii 50 to 1500 µm
Snow radius 1000 µm LAP conc. 10 to 500 ppmw
clean

## Slide 6
Mid-latitude winter atmos
Solar zenith = 60°
Elevation = 3000 m
Radiative forcing (spectral)
Snow radius 1000 µm LAP conc 500 ppmw

## Slide 7: Requirement addresses integration over solar spectrum
Integral of absorbed solar radiation over 280-4000 nm sensitive to grain size and light-absorbing particles
Define grain size accuracy in terms of the square root of the effective radius, whereas absorption vs. radius itself is nonlinear

## Slide 8
absorption = f(radius) is nonlinear
But absorption = f is nearly linear

## Slide 9
Why is dirty snow more sensitive to uncertainty in grain size?

## Slide 10
clean
dirty
Grain radius from 50 to 1500 µm, LAP conc. 200 ppmw
Radiative forcing: convolve spectral reflectance difference with solar spectrum and integrate over wavelength
Integrating albedo difference over 400-900 nm defines “darkening”

## Slide 11
Relationship is linear and about 0.8:1, so getting radiative forcing to ± 10% depends on getting darkening to ± 12%

## Slide 12: Recommendation to meet the specifications in the Decadal Survey
The Science/Applications Traceability Matrix for NASA’s SBG mission (Surface Biology and Geology) should:
  Specify that the sensor, data processing, and algorithms retrieve square root of effective radius of snow grains to within 18% RMS error
  And that the “darkening” of snow—the difference between estimated clean albedo and actual albedo integrated over wavelengths 400 to 900 nm—is retrieved to within 12% RMS error
  (these thresholds to be explored under a range of illumination conditions and fractional snow-covered area)
Effects of sensor calibration and atmospheric correction should be evaluated in this context

## Slide 13
Slides posted at https://snow.ucsb.edu

## Slide 14: Emails, just in case
Jeff: dozier@ucsb.edu
Ned: edward.h.bair@leidos.com
Niklas: urs.n.bohn@jpl.nasa.gov
David: david.r.thompson@jpl.nasa.gov